## Slide 1: Network Applications: Load Balancing among Homogeneous Servers
  Qiao Xiang, Congming Gao, Qiang Su
  https://sngroup.org.cn/courses/cnns-xmuf25/index.shtml
  10/16/2025
This deck of slides are heavily based on CPSC 433/533 at Yale University, by courtesy of Dr. Y. Richard Yang.

## Slide 2: Outline
Admin and recap
Multiple network servers

## Slide 3: Recap: Operational Laws
Utilization law: U = XS
Forced flow law: Xi = Vi X
Bottleneck device: largest Di = Vi Si
Little’s Law: Qi = Xi Ri
Bottleneck bound of interactive response (for the given closed model):

## Slide 4: Recap: Why Multiple Servers?
Scalability
  Scaling beyond single server throughput
    There is a fundamental limit on what a single server can
      process (CPU/bw/disk throughput)
      store (disk/memory)
  Scaling beyond single geo location latency
    There is a limit on the speed of light
    Network detour and delay further increase the delay
Notes: Facebook 12 M HTTP/sec
http://www.datadoghq.com/2013/07/the-best-of-velocity-and-devopsdays-2013-part-ii/

## Slide 5: Request Routing: Overview
Internet
- Global request routing: select a server site for each request
- Local request routing: select a specific server at the chosen site
Client
Site A
Site B
?

## Slide 6: Request Routing: Basic Architecture
server
state
net state: path property between servers/clients
server
selection algorithm
requests
notify client
about selection (direction mech.)

## Slide 7: Client Direction Mechanisms
Key difficulty
  May need to handle a large of clients
Basic types of mechanisms
  Application layer, e.g.,
    App/user is given a list of candidate server names
    HTTP redirector
  DNS: name resolution gives a list of server addresses
  IP layer: Same IP address represents multiple physical servers
    IP anycast: Same IP address shared by multiple servers and announced at different parts of the Internet. Network directs different clients to different servers
    Smart-switch indirection: a server IP address may be a virtual IP address for a cluster of physical servers

## Slide 8: Direction Mechanisms are Often Combined
Cluster2
in Europe
Cluster1 in US East
Cluster2
in US West
proxy
Load
balancer
Load
balancer
servers
DNS name1
IP1
IP2
IPn
DNS name2
App

## Slide 9: Example: Netflix

## Slide 10: Outline
Recap
Single network server
Multiple network servers
  Why multiple servers
  Request routing mechanisms
    Overview
    Application-layer
    DNS

## Slide 11: Basic DNS Indirection and Rotation
157.166.226.25
router
DNS server for cnn.com
IP address
of cnn.com
157.166.226.25
157.166.226.26
IP address
of cnn.com
157.166.226.26
157.166.226.25
157.166.226.26
157.166.255.18
%dig cnn.com

## Slide 12: CDN Using DNS (Akamai Architecture as an Example)
Content publisher (e.g., cnn)
  provides base HTML documents
  runs origin server(s); but delegates heavy-weight content (e.g., images) to CDN
Akamai runs
  (~240,000) edge servers for hosting content
    Deployment into 130 countries and 1600 networks
    Claims 85% Internet users are within a single "network hop" of an Akamai CDN server.
  customized DNS redirection servers to select edge servers based on
    closeness to client browser, server load
Source: https://www.akamai.com/us/en/about/facts-figures.jsp

## Slide 13: Linking to Akamai
Originally, URL Akamaization of embedded content: e.g.,
  <IMG SRC= http://www.provider.com/image.gif > changed to
<IMG SRC = http://a661. g.akamai.net/hash/image.gif>
URL Akamaization is becoming obsolete and supported mostly for legacy reasons
Note that this DNS redirection unit is per customer, not individual files.

## Slide 14: Exercise
Check any web page of nba.com and find a page with an image
Find the URL
Use %dig [+trace] to see DNS load direction
https://www.nba.com/news/reports-lakers-extend-gm-rob-pelinka-through-2025-26-season
https://cdn.nba.com/manage/2021/08/GettyImages-1234610091-scaled-e1665274852371-784x441.jpg
Notes: https://media.cnn.com/api/v1/images/stellar/prod/221007114404-01-kogi-nigeria-floods.jpg?c=16x9&q=h_720,w_1280,c_fill

## Slide 15: Exercise
https://cdn.nba.com/manage/2025/10/16x9-43.jpg?w=1568&h=882

## Slide 16: Recap: CNAME based DNS Name
Typical design
  Use cname to create aliases, e.g., https://cdn.nba.com/manage/2021/08/GettyImages-1234610091-scaled-e1665274852371-1568x882.jpg
  cname: e8017.dscb.akamaiedge.net
    why two levels in the name?

## Slide 17: Two-Level Direction
high-level DNS determines proximity, directs to low-level DNS;
low-level DNS: who manages a close-by cluster of servers with different IP addresses
Input: dscb.akamaiedge.net & and client IP,
Output: region (low-level) DNS
Input: e8017.dscb.akamaiedge.net & and client IP
Output: specific servers

## Slide 18: Akamai Load Direction
If the directed edge server does not have requested content,
it goes back to the original server (source) .
Notes: High-level DNS determines client location and forward to the corresponding low level DNS

## Slide 19: Two-Level DNS Mapping Alg
High-level
  Typically geo-location matching from client to reg
Low-level
  Typically secret, e.g., details of Akamai algorithms are proprietary
  Typical goal: load balancing among servers

## Slide 20: Akamai Local DNS LB Alg
A Bin-Packing algorithm (column 12 of Akamai Patent) every T second
  Compute the load to each publisher k (called serial number)
  Sort the publishers from increasing load
  For each publisher, associate a list of random servers generated by a hash function
    Hash range may be increasing, e.g., first hash [0,1], second [0, 3]
  Assign the publisher to the first server that does not overload

## Slide 21: Discussion
Advantages of using DNS for using multiple servers (LB)
  Leveraging existing DNS features (e.g., cname, hierarchy name for natural hierarchical redirection)
  Leveraging existing DNS deployment/optimization
Disadvantages of using DNS
  Distributed caching may lead to slow response
  Only in the unit of IP addresses

## Slide 22: Outline
Recap
Multiple network servers
  Basic issues
  Load direction
    DNS (IP level)
    Load balancer/smart switch (sub-IP level)

## Slide 23: Smart Switch: Big Picture
smart switch

## Slide 24: Load Balancer (LB): Basic Structure
LB
Client
Server1
Server2
Server3
Problem of the basic structure?
VIP
RIP1
RIP2
RIP3
D=VIP
S=client
D=VIP
S=client

## Slide 25: Problem
Client to server packet has VIP as destination address, but real servers use RIPs
  if LB just forwards the packet from client to a real server, the real server drops the packet
  reply from real server to client has real server IP as source -> client will drop the packet
state: listening
address: {RealIP.6789, *:*}
completed connection queue: C1; C2 sendbuf:
recvbuf:
state:
address: {VIP:6789, 198.69.10.10.1500}
sendbuf:
recvbuf:
state:
address: {RealIP:6789, 198.69.10.10.1500}
sendbuf:
recvbuf:
…
…
D=VIP
S=client
client
server

## Slide 26: Solution 1: Network Address Translation (NAT)
LB does rewriting/ translation
Thus, the LB is similar to a typical NAT gateway with an additional scheduling function
Load Balancer

## Slide 27: LB/NAT Advantages and Disadvantages
Advantages:
  Only one public IP address is needed for the load balancer; real servers can use private IP addresses
  Real servers need no change and are not aware of load balancing
Problem
  The load balancer must be on the critical path and hence may become the bottleneck due to load to rewrite request and response packets
    Typically, rewriting responses has more load because there are more response packets

## Slide 28: Goal: LB w/ Direct Reply
load
balancer
Connected
by a single switch

## Slide 29: LB with Direct Reply: Implication
LB
Client
Server1
Server2
Server3
Direct reply
VIP
VIP
Each real server uses VIP as its IP address
Address conflict: multiple devices w/ the same IP addr

## Slide 30: Why IP Address Matters?
Each network interface card listens to an assigned MAC address
A router is configured with the range of IP addresses connected to each interface (NIC)
To send to a device with a given IP, the router needs to translate IP to MAC (device) address
The translation is done by the Address Resolution Protocol (ARP)
VIP

## Slide 31: ARP Protocol
ARP is “plug-and-play”:
  nodes create their ARP tables without intervention from net administrator
A broadcast protocol:
  Router broadcasts query frame, containing queried IP address
    all machines on LAN receive ARP query
  Node with queried IP receives ARP frame, replies its MAC address

## Slide 32: ARP in Action
VIP
- Router broadcasts ARP broadcast query: who has VIP?
- ARP reply from LB: I have VIP; my MAC is MACLB
- Data packet from R to LB: destination MAC = MACLB
Router R
D=VIP
S=client

## Slide 33: LB/DR Problem
VIP
VIP
VIP
VIP
ARP and race condition:
When router R gets a packet with dest. address VIP, it broadcasts an Address Resolution Protocol (ARP) request: who has VIP?
One of the real servers may reply before load balancer
Solution: configure real servers to not respond to ARP request
Router R

## Slide 34: LB via Direct Routing
The virtual IP address is shared by real servers and the load balancer.
Each real server has a non-ARPing, loopback alias interface configured with the virtual IP address, and the load balancer has an interface configured with the virtual IP address to accept incoming packets.
The workflow of LB/DR is similar to that of LB/NAT:
  the load balancer directly routes a packet to the selected server
    the load balancer simply changes the MAC address of the data frame to that of the server and retransmits it on the LAN (how to know the real server’s MAC?)
  When the server receives the forwarded packet, the server determines that the packet is for the address on its loopback alias interface, processes the request, and finally returns the result directly to the user

## Slide 35: LB/DR Advantages and Disadvantages
Advantages:
  Real servers send response packets to clients directly, avoiding LB as bottleneck
Disadvantages:
  Servers must have non-arp alias interface
  The load balancer and server must have one of their interfaces in the same LAN segment
  Considered by some as a hack, not a clean architecture

## Slide 36: Example Implementation of LB
An example open source implementation is Linux virtual server (linux-vs.org)
    Used by
      www.linux.com
      sourceforge.net
      wikipedia.org
    More details on ARP problem: http://www.austintek.com/LVS/LVS-HOWTO/HOWTO/LVS-HOWTO.arp_problem.html
  Many commercial LB servers from F5, Cisco, …
More details please read chapter 2 of Load Balancing Servers, Firewalls, and Caches

## Slide 37: Problem of the Load Balancer Architecture
LB
Client
Server1
Server2
Server3
One major problem is that the LB becomes a single point of failure (SPOF).
VIP
D=VIP
S=client

## Slide 38: Solutions
Redundant load balancers
  E.g., two load balancers (a good question to think offline)
Fully distributed load balancing
  e.g., Microsoft Network Load Balancing (NLB)

## Slide 39: Microsoft NLB
No dedicated load balancer
All servers in the cluster receive all packets
Key issue: one and only one server processes each packet
  All servers within the cluster simultaneously run a mapping algorithm to determine which server should handle the packet. Those servers not required to service the packet simply discard it.
      Mapping (ranking) algorithm: computing the “winning” server according to host priorities, multicast or unicast mode, port rules, affinity, load percentage distribution, client IP address, client port number, other internal load information
  http://technet.microsoft.com/en-us/library/cc739506%28WS.10%29.aspx

## Slide 40: Discussion
Compare the design of using Load Balancer vs Microsoft NLB

## Slide 41: Recap: Direction Mechanisms
Cluster2
in Europe
Cluster1 in US East
Cluster2
in US West
proxy
Load
balancer
Load
balancer
servers
DNS name1
IP1
IP2
IPn
DNS name2
App
Rewrite
Direct reply
Fault tolerance

## Slide 42: Scalability of Server-Only Approaches
edge. servers
C0
client 1
client 2
client 3
client n
DNS
origin