## Slide 1: Statistical Multiplexing; Layered Network Architecture
This deck of slides are heavily based on CPSC 433/533 at Yale University, by courtesy of Dr. Y. Richard Yang.
  Qiao Xiang, Congming Gao, Qiang Su
  https://sngroup.org.cn/courses/cnns-xmuf25/index.shtml
  09/09/2025

## Slide 2: Outline
Admin. and recap
A taxonomy of communication networks
  circuit switching vs. packet switching
  datagram and virtual circuit packet switched networks
Layered network architecture

## Slide 3
Basic question: how are data (the bits) transferred through communication networks?
Recap: A Taxonomy of Comm. Networks
communication networks
switched networks
broadcast networks
circuit-switched networks (e.g. telephone, GSM)
packet-switched networks (e.g. Internet)

## Slide 4: Recap: Circuit Switching vs. Packet Switching
 | circuit switching | packet switching
resource usage | use a single partition bandwidth | use whole link bandwidth
reservation/setup | need reservation (setup delay) | no reservation
resource contention | busy signal (session loss) | congestion (long delay and packet losses)
charging | time | packet
header | no per-pkt header | per packet header
fast path processing | fast | per packet processing

## Slide 5: Queueing Theory
Strategy:
  model system state
    if we know the fraction of time that the system spends at each state, we can get answers to many basic questions: how long does a new request need to wait before being served?
System state changes upon events:
  introduce state transition diagram
  focus on equilibrium: state trend neither growing nor shrinking (key issue: how to define equilibrium)
Our approach: We are not interested in extremely precise modeling, but want quantitative intuition

## Slide 6: Warm up: Analysis of Circuit-Switching Blocking (Busy) Time
Assume a link has only a finite number of N circuits
Objective: compute the percentage of time that a new session (call) is blocked
Analogy in a more daily-life scenario?
Key parameters?
Notes: Key input parameters?

## Slide 7: Analysis of Circuit-Switching Blocking (Busy) Time
Consider a simple arrival pattern
  client requests arrive at a rate of  (lambda/second)
  service rate: each call takes on average 1/ second
Arrival and service patterns: memoryless (Markovian)
  During a small interval t, the number of expected new arrivals is: t
  During a small interval t, the chance (fraction) of a current call finishes is: t
This model is also called an M/M/N model

## Slide 8: Analysis of Circuit-Switching Blocking (Busy) Time: State
k+1
system state: # of busy lines
0
1
k
N
p0
p1
pk
pk+1
pN
Q: How to characterize equilibrium?

## Slide 9: Equilibrium = Time Reversibility [Frank Kelly]
Statistically cannot distinguish
time
state
k
k+1
=
=
=
Play the sequence backwards

## Slide 10: Analysis of Circuit-Switching Blocking (Busy) Time: Sketch
0
1
k
N
system state: # of busy lines
at equilibrium (time resersibility) in one unit time: #(transitions k  k+1) = #(transitions k+1  k)
p0
p1
pk
k+1
pk+1

(k+1)
pN

## Slide 11: Queueing Analysis: Packet Switching Delay
Four types of delay at each hop
  nodal processing delay: check errors & routing
  queueing: time waiting for its turn at output link
  transmission delay: time to pump packet onto a link at link speed
  propagation delay: router to router propagation
The focus is on queueing and transmission delay
system state?

## Slide 12: Packet Switching Delay
0
1
k
N
system state: #packets in queue
at equilibrium (time reversibility) in one unit time: #(transitions k  k+1) = #(transitions k+1  k)
p0
p1
pk
k+1
pk+1



## Slide 13: Summary: Queueing Theory
Model system state
Introduce state transition diagram
Focus on equilibrium: state trend neither growing nor shrinking

## Slide 14: Example
Assume requests (packets) come in at a rate of one request per 50 ms
Each request (packet) takes on average 20 ms
What is the fraction of time that the system is empty?
What is the chance that a packet newly arrived needs to wait for 3 early packets?
=1/50ms =20/s
=20 ms, =50/s
Notes: Rau = 2/3
(1-2/3)(2/3)^3 = 1/3 * 8/27 = 8/84 = 10%

## Slide 15: Analysis of Delay (cont’)
Average queueing delay:
Transmission delay:
Queueing + transmission:
0
1
k
k+1



## Slide 16
Delay
For a demo of M/M/1, see: http://www.dcs.ed.ac.uk/home/jeh/Simjava/queueing/mm1_q/mm1_q.html

## Slide 17
Queueing Delay as a Function of Utilization
 ~ 0: average queueing delay small
 -> 1: delay becomes large
 > 1: more “work” arriving than can be serviced, average delay infinite !

Assume:
R = link bandwidth (bps)
L = packet length (bits)
S = L / R
a = average packet arrival rate (pkt/sec)

## Slide 18: Statistical Multiplexing
no reservation: all arrivals into the single link, the queueing delay + transmission delay:
reservation: each flow uses its own reserved (sub)link with rate /n, the queueing delay + transmission delay:
A simple model to compare bandwidth efficiency of
- reservation/dedication (aka circuit-switching) vs
- no reservation (aka packet switching) setup
- a single bottleneck link with
service rate
- flows; each flow has an arrival rate of
For each flow i:

## Slide 19
Summary: Packet Switching vs. Circuit Switching
Advantages of packet switching over circuit switching
  most important advantage of packet-switching over circuit switching is statistical multiplexing, and therefore more efficient bandwidth usage
Disadvantages of packet switching
  potential congestion: packet delay and high loss
    protocols needed for reliable data transfer, congestion control
    it is possible to guarantee quality of service (QoS) in packet-switched networks and still gain statistical multiplexing, but it adds much complexity
  packet header overhead
  per packet processing overhead

## Slide 20
Outline
Admin. and recap
A taxonomy of communication networks
  circuit switched networks
  packet switched networks
  circuit switching vs. packet switching
  datagram and virtual circuit packet switched networks

## Slide 21
A Taxonomy of Packet-Switched Networks According to Routing
Two types of packet switching
  datagram network
    each packet of a flow is switched independently
  virtual circuit network:
    all packets from one flow are sent along a pre-established path (= virtual circuit)

## Slide 22: Datagram Packet Switching
Commonly when we say packet switching we mean datagram switching
Example: IP networks
Each packet is independently switched
  each packet header contains complete destination address
  receiving a packet, a router looks at the packet’s destination address and searches its current routing table to determine the possible next hops, and pick one
Analogy: postal mail system
Notes:   Disadvantages: routes may change during session
  Advantage: routers do not keep any state about a flow;
  thus, network architecture is
    robust
    scalable

## Slide 23
Host A
Host B
Host E
Host D
Host C
Node 1
Node 2
Node 3
Node 4
Node 5
Node 6
Node 7
Datagram Packet Switching

## Slide 24: Timing Diagram of Datagram Switching
Packet 1
Packet 2
Packet 3
Packet 1
Packet 2
Packet 3
Packet 1
Packet 2
Packet 3
Host A
Host B
Node 1
Node 2
propagation
delay from
Host A to
Node 1
transmission
time of Packet 1
at Host A

## Slide 25: Virtual-Circuit Packet Switching
Example: Multiple Label Packet Switching (MPLS) in IP networks
Hybrid of circuit switching and datagram switching
  fixed path determined at virtual circuit setup time, remains fixed thru flow
  Implementation:
    each packet carries a short local, tag (virtual-circuit (VC) #); tag determines next hop
Incoming VC# | Outgoing Interface | QoS
12 | 2 | 
16 | 3 | 
20 | 3 | 
… |  | 

## Slide 26
Host A
Host B
Host E
Host D
Host C
Node 1
Node 2
Node 3
Node 4
Node 5
Node 6
Node 7
Virtual-Circuit Switching

## Slide 27: Virtual-Circuit Packet Switching
Three phases
  VC establishment
  Data transfer
  VC disconnect

## Slide 28: Timing Diagram of Virtual-Circuit Switching
Packet 1
Packet 2
Packet 3
Packet 1
Packet 2
Packet 3
Packet 1
Packet 2
Packet 3
Host 1
Host 2
Node 1
Node 2
propagation delay
between Host 1
and Node 1
VC
establishment
VC
termination
data
transfer

## Slide 29: Discussion: Datagram Switching vs. Virtual Circuit Switching
What are the benefits of datagram switching over virtual circuit switching?
What are the benefits of virtual circuit switching over datagram switching?
Notes: What advantages do virtual circuit have over datagram?
can treat different flows differently, if flows setup its desired treatment
  Guarantees in-sequence delivery of packets
  However: Packets from different virtual circuits may be interleaved

## Slide 30
Summary of the Taxonomy of Communication Networks
circuit-switched network
communication network
switched network
broadcast communication
packet-switched network
datagram network
virtual circuit network

## Slide 31: Summary of Progress
We have seen the hardware infrastructure, the basic communication scheme, a next key question is how to develop the software system.

## Slide 32: Summary of Progress
We have seen the hardware infrastructure, the basic communication scheme, a next key question is how to develop the software system.

## Slide 33
Outline
Admin. and recap
A taxonomy of communication networks
Layered network architecture
  what is layering?
  why layering?
  how to determine the layers?
  ISO/OSI layering and Internet layering

## Slide 34
A technique to organize a networked system into a succession of logically distinct entities, such that the service provided by one entity is solely based on the service provided by the previous (lower level) entity.
What is Layering?
Application
Transport
Network
Datalink
Physical
Application
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Physical medium

## Slide 35
Outline
Admin. and recap
A taxonomy of communication networks
Layered network architecture
  what is layering?
  why layering?

## Slide 36
Why Layering?
Dealing with complex systems: explicit structure allows identification of the relationship among a complex system’s pieces
  layered reference model for discussion
Networks are complex !
many “pieces”:
  hardware
    hosts
    routers
    links of various media
  software
    applications
    infrastructure
Modularization eases maintenance, updating of system:
  change of implementation of a layer’s service transparent to rest of system, e.g., changes in routing protocol doesn’t affect rest of system

## Slide 37: An Example: No Layering
No layering: each new application has to be re-implemented for every network technology !
Telnet
FTP
Wireless
Ether-net
Fiber
optic
Application
Transmission
Media
HTTP

## Slide 38: An Example: Benefit of Layering
Introducing an intermediate layer provides a common abstraction for network technologies
HTTP
Telnet
FTP
Wireless
Ethernet
Fiber
optic
Application
Transmission
Media
Transport
& Network

## Slide 39
ISO/OSI Concepts
ISO – International Standard Organization
OSI – Open System Interconnection
Service – says what a layer does
Interface – says how to access the service
Protocol – specifies how the service is implemented
  a set of rules and formats that govern the communications between two or more peers

## Slide 40: An Example of Layering

## Slide 41: An Example of Layering

## Slide 42: Layering -> Logical Communication
E.g.: application
provide services to users
application protocol:
  send messages to peer
  for example, HELO, MAIL FROM, RCPT TO are messages between two SMTP peers

## Slide 43
Layering: Logical Communication
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
data
data
E.g.: transport
Trans. msg for app
Transport protocol
  add control info to form “segment”
  send segment to peer
  wait for peer to ack receipt; if no ack, retransmit
data
transport
transport
ack

## Slide 44
Layering: Physical Communication
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
data
data

## Slide 45
Protocol Layering and Meta Data
Each layer takes data from above
adds header (meta) information to its peer to create new data unit
passes new data unit to layer below

## Slide 46: Packet as a Stack in a Layered Architecture
Application
Transport
Network
Datalink
Physical
Application
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Physical medium

## Slide 47: Some Implications of Layered Architecture
A packet as a stack container
Each layer needs multiplexing and demultiplexing to serve layer above
Hn
Hn-1
…
Ln-1
Has a field to indicate which higher layer requires the service
Ln

## Slide 48
Key design issue:
How do you divide functionalities among the layers?

## Slide 49
Admin. and recap
A taxonomy of communication networks
Layered network architecture
  what is layering?
  why layering?
  how to determine the layers?
Outline

## Slide 50
The End-to-End Arguments
The function in question can completely and correctly be implemented only with the knowledge and help of the application standing at the endpoints of the communication systems. Therefore, providing that questioned function as a feature of the communications systems itself is not possible.
J. Saltzer, D. Reed, and D. Clark, 1984

## Slide 51
What does the End-to-End Arguments Mean?
The application knows the requirements best, place functionalities as high in the layer as possible
Think twice before implementing a functionality at a lower layer, even when you believe it will be useful to an application

## Slide 52
Example: Where to Provide Reliability ?
Solution 1: the network (lower layer L1) provides reliability, i.e., each hop provides reliability
Solution 2: the end host (higher layer L2) provides reliability, i.e., end-to-end check and retry
L1
L2
L1
S
R
L1
L2
A

## Slide 53
What are Reasons for Implementing Reliability at Higher Layer ?
The lower layer cannot completely provide the functionality
  the receiver has to do the check anyway !
Implementing it at lower layer increases complexity, cost and overhead at lower layer
  shared by all upper layer applications  everyone pays for it, even if you do not need it
The upper layer
  knows the requirements better and thus may choose a better approach to implement it
L1
L2
L1
S
R
L1
L2
A
Notes: First point: L1 may first ack and then crash; then the function fails; if L2 crash; the application crashes also->fate sharing

## Slide 54
Are There Reasons Implementing Reliability at Lower Layer ?
Improve performance, e.g., if high cost/delay/… on a local link
  improves efficiency
  reduces delay
Share common code, e.g., reliability is required by multiple applications
L1
L2
L1
S
R
L1
L2
A
Notes: S to A: San francisco to Yale router
A to R: Yale router to a wireless laptop (e.g., 10% success rate)

## Slide 55: Summary: End-to-End Arguments
If a higher layer can do it, don’t do it at a lower layer -- the higher the layer, the more it knows about the best what it needs
Add functionality in lower layers iff it
    (1) is used by and improves performance of a large number of (current and potential future) applications,
    (2) does not hurt (too much) other applications, and
    (3) does not increase (too much) complexity/overhead
Practical tradeoff, e.g.,
  allow multiple interfaces at a lower layer (one provides the function; one does not)
Notes: Issue: does not reduce complexity/cost
upper layer needs to be developed for all interfaces

## Slide 56
We used reliability as an example
Assume two layers (L1: network; L2: end-to-end). Where may you implement the following functions?
  security (privacy of traffic)
  quality of service (e.g., delay/bandwidth guarantee)
  congestion control (e.g., not to overwhelm network links or receiver)
Examples
L1
L2
L1
S
R
L1
L2
A

## Slide 57: Example
Consider the presence service in a social networking system: shows which contacts are online (e.g., skype)
  implementing by end user’s host app or through a third party service?
L2
L1
A
B
L2

## Slide 58: Challenges
Challenges to build a good (networking) system: find the right balance between:
reuse, interoperability, implementation effort
(apply layering concepts)
end-to-end arguments
performance
No universal answer: the answer depends on the goals and assumptions!

## Slide 59: Discussion: Limitations of Layered Architecture